## Slide 1: Computer Architecture and Logic Design (CALD) Lecture 08
Engr.Ramsha Mashood
Senior Lecturer
Department of Software Engineering
Bahria University Karachi Campus
Email: ramshamashood.bukc@bahria.edu.pk

## Slide 2: Processor Structure and Function

## Slide 3: Processor Organization
Fetch instruction
  The processor reads an instruction from memory (register, cache, main memory)
Interpret instruction
  The instruction is decoded to determine what action is required
Fetch data
  The execution of an instruction may require reading data from memory or an I/O module
Process data
  The execution of an instruction may require performing some arithmetic or logical operation on data
Write data
  The results of an execution may require writing data to memory or an I/O module
In order to do these things the processor needs to store some data temporarily and therefore needs a small internal memory
Processor Requirements:
Notes: 22
To understand the organization of the processor, let us consider the requirements placed on the processor, the things that it must do:
Fetch instruction: The processor reads an instruction from memory (register, cache, main memory).
Interpret instruction: The instruction is decoded to determine what action is required.
Fetch data: The execution of an instruction may require reading data from memory or an I/O module.
Process data: The execution of an instruction may require performing some arithmetic or logical operation on data.
Write data: The results of an execution may require writing data to memory or an I/O module.
To do these things, it should be clear that the processor needs to store some data temporarily. It must remember the location of the last instruction so that it can know where to get the next instruction. It needs to store instructions and data temporarily while an instruction is being executed. In other words, the processor needs a small internal memory.

## Slide 4
Notes: Figure 14.1 is a simplified view of a processor, indicating its connection to the rest of the system via the system bus. A similar interface would be needed for any of the interconnection structures described in Chapter 3. The reader will recall that the major components of the processor are an arithmetic and logic unit (ALU) and a control unit (CU). The ALU does the actual computation or processing of data. The control unit controls the movement of data and instructions into and out of the processor and controls the operation of the ALU. In addition, the figure shows a minimal internal memory, consisting of a set of storage locations, called registers.

## Slide 5
Notes: Figure 14.2 is a slightly more detailed view of the processor. The data transfer and logic control paths are indicated, including an element labeled internal processor bus. This element is needed to transfer data between the various registers and the ALU because the ALU in fact operates only on data in the internal processor memory. The figure also shows typical basic elements of the ALU. Note the similarity between the internal structure of the computer as a whole and the internal structure of the processor. In both cases, there is a small collection of major elements (computer: processor, I/O, memory; processor: control unit, ALU, registers) connected by data paths.

## Slide 6: Register Organization
Enable the machine or assembly language programmer to minimize main memory references by optimizing use of registers
Used by the control unit to control the operation of the processor and by privileged operating system programs to control the execution of programs
User-Visible Registers
Control and Status Registers
Within the processor there is a set of registers that function as a level of memory above main memory and cache in the hierarchy
The registers in the processor perform two roles:
Notes: 23
As we discussed in Chapter 4, a computer system employs a memory hierarchy. At higher levels of the hierarchy, memory is faster, smaller, and more expensive (per bit). Within the processor, there is a set of registers that function as a level of memory above main memory and cache in the hierarchy. The registers in the processor perform two roles:
User-visible registers: Enable the machine- or assembly language programmer to minimize main memory references by optimizing use of registers.
Control and status registers: Used by the control unit to control the operation of the processor and by privileged, operating system programs to control the execution of programs.
There is not a clean separation of registers into these two categories. For example, on some machines the program counter is user visible (e.g., x86), but on many it is not. For purposes of the following discussion, however, we will use these categories.

## Slide 7: User-Visible Registers
Referenced by means of the machine language that the processor executes
Categories:
General purpose
Can be assigned to a variety of functions by the programmer
Data
May be used only to hold data and cannot be employed in the calculation of an operand address
Address
May be somewhat general purpose or may be devoted to a particular addressing mode
Examples: segment pointers, index registers, stack pointer
Condition codes
Also referred to as flags
Bits set by the processor hardware as the result of operations
Notes: 24
A user-visible register is one that may be referenced by means of the machine language that the processor executes. We can characterize these in the following categories:
  General purpose
  Data
  Address
  Condition codes
  General-purpose registers can be assigned to a variety of functions by the programmer. Sometimes their use within the instruction set is orthogonal to the operation. That is, any general-purpose register can contain the operand for any opcode. This provides true general-purpose register use. Often, however, there are restrictions. For example, there may be dedicated registers for floating-point and stack operations.
  In some cases, general-purpose registers can be used for addressing functions (e.g., register indirect, displacement). In other cases, there is a partial or clean separation between data registers and address registers. Data registers may be used only to hold data and cannot be employed in the calculation of an operand address.
Address registers may themselves be somewhat general purpose, or they may be
devoted to a particular addressing mode. Examples include the following:
Segment pointers: In a machine with segmented addressing (see Section 8.3), a segment register holds the address of the base of the segment. There may be multiple registers: for example, one for the operating system and one for the current process.
Index registers: These are used for indexed addressing and may be autoindexed.
Stack pointer: If there is user-visible stack addressing, then typically there is a dedicated register that points to the top of the stack. This allows implicit ad- dressing; that is, push, pop, and other stack instructions need not contain an explicit stack operand.
There are several design issues to be addressed here. An important issue is whether to use completely general-purpose registers or to specialize their use. We have already touched on this issue in the preceding chapter because it affects instruction set design. With the use of specialized registers, it can generally be implicit in the opcode which type of register a certain operand specifier refers to. The operand specifier must only identify one of a set of specialized registers rather than one out of all the registers, thus saving bits. On the other hand, this specialization limits the programmer’s flexibility.
Another design issue is the number of registers, either general purpose or data plus address, to be provided. Again, this affects instruction set design because more registers require more operand specifier bits. As we previously discussed, somewhere between 8 and 32 registers appears optimum [LUND77]. Fewer registers result in more memory references; more registers do not noticeably reduce memory references (e.g., see [WILL90]). However, a new approach, which finds advantage in the use of hundreds of registers, is exhibited in some RISC systems and is discussed in Chapter 15.
Finally, there is the issue of register length. Registers that must hold addresses obviously must be at least long enough to hold the largest address. Data registers should be able to hold values of most data types. Some machines allow two contiguous registers to be used as one for holding double-length values.
A final category of registers, which is at least partially visible to the user, holds condition codes (also referred to as flags). Condition codes are bits set by the processor hardware as the result of operations. For example, an arithmetic operation may produce a positive, negative, zero, or overflow result. In addition to the result itself being stored in a register or memory, a condition code is also set. The code may subsequently be tested as part of a conditional branch operation.
Condition code bits are collected into one or more registers. Usually, they form part of a control register. Generally, machine instructions allow these bits to be read by implicit reference, but the programmer cannot alter them.

## Slide 8: Condition Codes
Notes: 27
Many processors, including those based on the IA-64 architecture and the MIPS processors, do not use condition codes at all. Rather, conditional branch instructions specify a comparison to be made and act on the result of the comparison, without storing a condition code. Table 14.1, based on [DERO87], lists key advantages and disadvantages of condition codes.
In some machines, a subroutine call will result in the automatic saving of all user-visible registers, to be restored on return. The processor performs the saving and restoring as part of the execution of call and return instructions. This allows each subroutine to use the user-visible registers independently. On other machines, it is the responsibility of the programmer to save the contents of the relevant user- visible registers prior to a subroutine call, by including instructions for this purpose in the program.

## Slide 9: Control and Status Registers
Program counter (PC)
  Contains the address of an instruction to be fetched
Instruction register (IR)
  Contains the instruction most recently fetched
Memory address register (MAR)
  Contains the address of a location in memory
Memory buffer register (MBR)
  Contains a word of data to be written to memory or the word most recently read
Four registers are essential to instruction execution:
Notes: 30
There are a variety of processor registers that are employed to control the operation of the processor. Most of these, on most machines, are not visible to the user. Some of them may be visible to machine instructions executed in a control or operating system mode.
Of course, different machines will have different register organizations and use different terminology. We list here a reasonably complete list of register types, with a brief description.
Four registers are essential to instruction execution:
Program counter (PC): Contains the address of an instruction to be fetched.
Instruction register (IR): Contains the instruction most recently fetched.
Memory address register (MAR): Contains the address of a location in memory.
Memory buffer register (MBR): Contains a word of data to be written to memory or the word most recently read.
Not all processors have internal registers designated as MAR and MBR, but some equivalent buffering mechanism is needed whereby the bits to be transferred to the system bus are staged and the bits to be read from the data bus are temporarily stored.
Typically, the processor updates the PC after each instruction fetch so that the PC always points to the next instruction to be executed. A branch or skip instruction will also modify the contents of the PC. The fetched instruction is loaded into an IR, where the opcode and operand specifiers are analyzed. Data are exchanged with memory using the MAR and MBR. In a bus- organized system, the MAR connects directly to the address bus, and the MBR connects directly to the data bus. User-visible registers, in turn, exchange data with the MBR.
The four registers just mentioned are used for the movement of data between the processor and memory. Within the processor, data must be presented to the ALU for processing. The ALU may have direct access to the MBR and user-visible registers. Alternatively, there may be additional buffering registers at the boundary to the ALU; these registers serve as input and output registers for the ALU and exchange data with the MBR and user-visible registers.

## Slide 10: Program Status Word (PSW)
Register or set of registers that contain status information
Common fields or flags include:
Sign
Zero
Carry
Equal
Overflow
Interrupt Enable/Disable
Supervisor
Notes: 31
Many processor designs include a register or set of registers, often known as the program status word (PSW), that contain status information. The PSW typically contains condition codes plus other status information. Common fields or flags include the following:
Sign: Contains the sign bit of the result of the last arithmetic operation.
Zero: Set when the result is 0.
Carry: Set if an operation resulted in a carry (addition) into or borrow (sub- traction) out of a high-order bit. Used for multiword arithmetic operations.
Equal: Set if a logical compare result is equality.
Overflow: Used to indicate arithmetic overflow.
Interrupt Enable/Disable: Used to enable or disable interrupts.
Supervisor: Indicates whether the processor is executing in supervisor or user mode. Certain privileged instructions can be executed only in supervisor mode, and certain areas of memory can be accessed only in supervisor mode.

## Slide 11: Common Flags in PSW Register
Sign: Contains the sign bit of the result of the last arithmetic operation.
Zero: Set when the result is 0.
Carry: Set if an operation resulted in a carry (addition) into or borrow (sub- traction) out of a high-order bit. Used for multiword arithmetic operations.
Equal: Set if a logical compare result is equality.
Overflow: Used to indicate arithmetic overflow.
Interrupt Enable/Disable: Used to enable or disable interrupts.
Supervisor: Indicates whether the processor is executing in supervisor or user mode. Certain privileged instructions can be executed only in supervisor mode, and certain areas of memory can be accessed only in supervisor mode.

## Slide 12
Notes: It is instructive to examine and compare the register organization of comparable systems. In this section, we look at two 16-bit microprocessors that were designed at about the same time: the Motorola MC68000 [STRI79] and the Intel 8086 [MORS78]. Figures 14.3a and b depict the register organization of each; purely internal registers, such as a memory address register, are not shown.
The MC68000 partitions its 32-bit registers into eight data registers and nine address registers. The eight data registers are used primarily for data manipulation and are also used in addressing as index registers. The width of the registers allows 8-, 16-, and 32-bit data operations, determined by opcode. The address registers contain 32-bit (no segmentation) addresses; two of these registers are also used as stack pointers, one for users and one for the operating system, depending on the current execution mode. Both registers are numbered 7, because only one can be used at a time. The MC68000 also includes a 32-bit program counter and a 16-bit status register.
The Intel 8086 takes a different approach to register organization. Every register is special purpose, although some registers are also usable as general purpose. The 8086 contains four 16-bit data registers that are addressable on a byte or 16-bit basis, and four 16-bit pointer and index registers. The data registers can be used as general purpose in some instructions. In others, the registers are used implicitly. For example, a multiply instruction always uses the accumulator. The four pointer registers are also used implicitly in a number of operations; each contains a segment offset. There are also four 16-bit segment registers. Three of the four segment registers are used in a dedicated, implicit fashion, to point to the segment of the current instruction (useful for branch instructions), a segment containing data, and a segment containing a stack, respectively. These dedicated and implicit uses provide for compact encoding at the cost of reduced flexibility. The 8086 also includes an instruction pointer and a set of 1-bit status and control flags.
The point of this comparison should be clear. There is no universally accepted philosophy concerning the best way to organize processor registers [TOON81]. As with overall instruction set design and so many other processor design issues, it is still a matter of judgment and taste.
A second instructive point concerning register organization design is illustrated in Figure 14.3c. This figure shows the user-visible register organization for the Intel 80386 [ELAY85], which is a 32-bit microprocessor designed as an extension of the 8086. The 80386 uses 32-bit registers. However, to provide upward compatibility for programs written on the earlier machine, the 80386 retains the original register organization embedded in the new organization. Given this design constraint, the architects of the 32-bit processors had limited flexibility in designing the register organization.

## Slide 13: Instruction Cycle
Includes the following stages:
Fetch
Read the next instruction from memory into the processor
Execute
Interpret the opcode and perform the indicated operation
Interrupt
If interrupts are enabled and an interrupt has occurred, save the current process state and service the interrupt
Notes: 35
In Section 3.2, we described the processor’s instruction cycle (Figure 3.9). To recall, an instruction cycle includes the following stages:
Fetch: Read the next instruction from memory into the processor.
Execute: Interpret the opcode and perform the indicated operation.
Interrupt: If interrupts are enabled and an interrupt has occurred, save the current process state and service the interrupt.
We are now in a position to elaborate somewhat on the instruction cycle. First, we must introduce one additional stage, known as the indirect cycle.

## Slide 14
Notes: Another way to view this process is shown in Figure 14.5, which is a revised version of Figure 3.12. This illustrates more correctly the nature of the instruction cycle. Once an instruction is fetched, its operand specifiers must be identified. Each input operand in memory is then fetched, and this process may require indirect addressing. Register-based operands need not be fetched. Once the opcode is executed, a similar process may be needed to store the result in main memory.

## Slide 15: Pipelining Strategy
Similar to the use of an assembly line in a manufacturing plant
New inputs are accepted at one end before previously accepted inputs appear as outputs at the other end
To apply this concept to instruction execution we must recognize that an instruction has a number of stages
Notes: 38
Instruction pipelining is similar to the use of an assembly line in a manufacturing plant. An assembly line takes advantage of the fact that a product goes through various stages of production. By laying the production process out in an assembly line, products at various stages can be worked on simultaneously. This process is also referred to as pipelining, because, as in a pipeline, new inputs are accepted at one end before previously accepted inputs appear as outputs at the other end.
To apply this concept to instruction execution, we must recognize that, in fact, an instruction has a number of stages. Figures 14.5, for example, breaks the instruction cycle up into 10 tasks, which occur in sequence. Clearly, there should be some opportunity for pipelining.

## Slide 16: Pipelining
Pipelining is an implementation technique whereby multiple instructions are overlapped in execution
Today, pipelining is the key implementation technique used to make fast CPUs
A pipeline is like an assembly line
  Each step operates in parallel with the other steps
In a computer pipeline, each step in the pipeline completes a part of an instruction

## Slide 17: Instruction Pipeline
Notes: As a simple approach, consider subdividing instruction processing into two stages: fetch instruction and execute instruction. There are times during the execution of an instruction when main memory is not being accessed. This time could be used to fetch the next instruction in parallel with the execution of the current one. Figure 14.9a depicts this approach. The pipeline has two independent stages. The first stage fetches an instruction and buffers it. When the second stage is free, the first stage passes it the buffered instruction. While the second stage is executing the instruction, the first stage takes advantage of any unused memory cycles to fetch and buffer the next instruction. This is called instruction prefetch or fetch overlap. Note that this approach, which involves instruction buffering, requires more registers. In general, pipelining requires registers to store data between stages.
It should be clear that this process will speed up instruction execution. If the fetch and execute stages were of equal duration, the instruction cycle time would be halved. However, if we look more closely at this pipeline (Figure 14.9b), we will see that this doubling of execution rate is unlikely for two reasons:
The execution time will generally be longer than the fetch time. Execution will involve reading and storing operands and the performance of some operation. Thus, the fetch stage may have to wait for some time before it can empty its buffer.
A conditional branch instruction makes the address of the next instruction to be fetched unknown. Thus, the fetch stage must wait until it receives the next instruction address from the execute stage. The execute stage may then have to wait while the next instruction is fetched.
Guessing can reduce the time loss from the second reason. A simple rule is the following: When a conditional branch instruction is passed on from the fetch to the execute stage, the fetch stage fetches the next instruction in memory after the branch instruction. Then, if the branch is not taken, no time is lost. If the branch is taken, the fetched instruction must be discarded and a new instruction fetched.

## Slide 18: Additional Stages
Fetch instruction (FI)
  Read the next expected instruction into a buffer
Decode instruction (DI)
  Determine the opcode and the operand specifiers
Calculate operands (CO)
  Calculate the effective address of each source operand
  This may involve displacement, register indirect, indirect, or other forms of address calculation
Fetch operands (FO)
  Fetch each operand from memory
  Operands in registers need not be fetched
Execute instruction (EI)
  Perform the indicated operation and store the result, if any, in the specified destination operand location
Write operand (WO)
  Store the result in memory
Notes: While these factors reduce the potential effectiveness of the two-stage pipe- line, some speedup occurs. To gain further speedup, the pipeline must have more stages. Let us consider the following decomposition of the instruction processing.
Fetch instruction (FI): Read the next expected instruction into a buffer.
Decode instruction (DI): Determine the opcode and the operand specifiers.
Calculate operands (CO): Calculate the effective address of each source operand. This may involve displacement, register indirect, indirect, or other forms of address calculation.
Fetch operands (FO): Fetch each operand from memory. Operands in registers need not be fetched.
Execute instruction (EI): Perform the indicated operation and store the result, if any, in the specified destination operand location.
Write operand (WO): Store the result in memory.
With this decomposition, the various stages will be of more nearly equal duration.

## Slide 19
Notes: 39
For the sake of illustration, let us assume equal duration. Using this assumption, Figure 14.10 shows that a six-stage pipeline can reduce the execution time for 9 instructions from 54 time units to 14 time units.
Several comments are in order: The diagram assumes that each instruction goes through all six stages of the pipeline. This will not always be the case. For example, a load instruction does not need the WO stage. However, to simplify the pipeline hardware, the timing is set up assuming that each instruction requires all six stages. Also, the diagram assumes that all of the stages can be performed in parallel. In particular, it is assumed that there are no memory conflicts. For example, the FI, FO, and WO stages involve a memory access. The diagram implies that all these accesses can occur simultaneously. Most memory systems will not permit that. However, the desired value may be in cache, or the FO or WO stage may be null. Thus, much of the time, memory conflicts will not slow down the pipeline.

## Slide 20
Notes: 40
Several other factors serve to limit the performance enhancement. If the six stages are not of equal duration, there will be some waiting involved at various pipe- line stages, as discussed before for the two-stage pipeline. Another difficulty is the conditional branch instruction, which can invalidate several instruction fetches. A similar unpredictable event is an interrupt. Figure 14.11 illustrates the effects of the conditional branch, using the same program as Figure 14.10. Assume that instruction 3 is a conditional branch to instruction 15. Until the instruction is executed, there is no way of knowing which instruction will come next. The pipeline, in this example, simply loads the next instruction in sequence (instruction 4) and proceeds. In Figure 14.10, the branch is not taken, and we get the full performance benefit of the enhancement. In Figure 14.11, the branch is taken. This is not determined until the end of time unit 7. At this point, the pipeline must be cleared of instructions that are not useful. During time unit 8, instruction 15 enters the pipeline. No instructions complete during time units 9 through 12; this is the performance penalty incurred because we could not anticipate the branch.

## Slide 21
Notes: Figure 14.12 indicates the logic needed for pipelining to account for branches and interrupts.
Other problems arise that did not appear in our simple two-stage organization. The CO stage may depend on the contents of a register that could be altered by a previous instruction that is still in the pipeline. Other such register and memory conflicts could occur. The system must contain logic to account for this type of conflict.

## Slide 22
Notes: To clarify pipeline operation, it might be useful to look at an alternative depiction. Figures 14.10 and 14.11 show the progression of time horizontally across the figures, with each row showing the progress of an individual instruction. Figure 14.13 shows same sequence of events, with time progressing vertically down the figure, and each row showing the state of the pipeline at a given point in time. In Figure 14.13a (which corresponds to Figure 14.10), the pipeline is full at time 6, with 6 different instructions in various stages of execution, and remains full through time 9; we assume that instruction I9 is the last instruction to be executed. In Figure 14.13b, (which corresponds to Figure 14.11), the pipeline is full at times 6 and 7. At time 7, instruction 3 is in the execute stage and executes a branch to instruction 15. At this point, instructions I4 through I7 are flushed from the pipeline, so that at time 8, only two instructions are in the pipeline, I3 and I15.

## Slide 23: Pipeline Hazards
Occur when the pipeline, or some portion of the pipeline, must stall because conditions do not permit continued execution
Also referred to as a pipeline bubble
There are three types of hazards:
Resource
Data
Control
Notes: In the previous subsection, we mentioned some of the situations that can result in less than optimal pipeline performance. In this subsection, we examine this issue in a more systematic way. Chapter 16 revisits this issue, in more detail, after we have introduced the complexities found in superscalar pipeline organizations.
A pipeline hazard occurs when the pipeline, or some portion of the pipeline, must stall because conditions do not permit continued execution. Such a pipe- line stall is also referred to as a pipeline bubble. There are three types of hazards: resource, data, and control.

## Slide 24: Resource Hazards
A resource hazard occurs when two (or more) instructions that are already in the pipeline need the same resource.
The result is that the instructions must be executed in serial rather than parallel for a portion of the pipeline.
A resource hazard is sometime referred to as a structural hazard.

## Slide 25
Notes: A resource hazard occurs when two (or more) instructions that are already in the pipeline need the same resource. The result is that the instructions must be executed in serial rather than parallel for a portion of the pipeline. A resource hazard is sometime referred to as a structural hazard.
Let us consider a simple example of a resource hazard. Assume a simplified five-stage pipeline, in which each stage takes one clock cycle. Figure 14.15a shows the ideal case, in which a new instruction enters the pipeline each clock cycle. Now assume that main memory has a single port and that all instruction fetches and data reads and writes must be performed one at a time. Further, ignore the cache. In this case, an operand read to or write from memory cannot be performed in parallel with an instruction fetch. This is illustrated in Figure 14.15b, which assumes that the source operand for instruction I1 is in memory, rather than a register. Therefore, the fetch instruction stage of the pipeline must idle for one cycle before beginning the instruction fetch for instruction I3. The figure assumes that all other operands are in registers.
Another example of a resource conflict is a situation in which multiple instructions are ready to enter the execute instruction phase and there is a single ALU. One solutions to such resource hazards is to increase available resources, such as having multiple ports into main memory and multiple ALU units.

## Slide 26: Resource Hazards
Assume that main memory has a single port and that all instruction fetches and data reads and writes must be performed one at a time.
An operand read to or write from memory cannot be performed in parallel with an instruction fetch.
This is illustrated in Figure 14.15b, which assumes that the source operand for instruction I1 is in memory, rather than a register.
Therefore, the fetch instruction stage of the pipeline must idle for one cycle before beginning the instruction fetch for instruction I3.
The figure assumes that all other operands are in registers.

## Slide 27: Resource Hazards
Another example of a resource conflict is a situation in which multiple instructions are ready to enter the execute instruction phase and there is a single ALU.
One solutions to such resource hazards is to increase available resources, such as having multiple ports into main memory and multiple ALU units.

## Slide 28: Data Hazards
A data hazard occurs when there is a conflict in the access of an operand location.
In general terms, we can state the hazard in this form:
  Two instructions in a program are to be executed in sequence and both access a particular memory or register operand.
  If the two instructions are executed in strict sequence, no problem occurs.
  However, if the instructions are executed in a pipeline, then it is possible for the operand value to be updated in such a way as to produce a different result than would occur with strict sequential execution.
  In other words, the program produces an incorrect result because of the use of pipelining.

## Slide 29
Notes: A data hazard occurs when there is a conflict in the access of an operand location. In general terms, we can state the hazard in this form: Two instructions in a program are to be executed in sequence and both access a particular memory or register operand. If the two instructions are executed in strict sequence, no problem occurs. However, if the instructions are executed in a pipeline, then it is possible for the operand value to be updated in such a way as to produce a different result than would occur with strict sequential execution. In other words, the program produces an incorrect result because of the use of pipelining.
As an example, consider the following x86 machine instruction sequence:
ADD EAX, EBX /* EAX = EAX + EBX
SUB ECX, EAX /* ECX = ECX – EAX
The first instruction adds the contents of the 32-bit registers EAX and EBX
and stores the result in EAX. The second instruction subtracts the contents of EAX
from ECX and stores the result in ECX. Figure 14.16 shows the pipeline behavior.

## Slide 30: Types of Data Hazard
Read after write (RAW), or true dependency
  An instruction modifies a register or memory location
  Succeeding instruction reads data in memory or register location
  Hazard occurs if the read takes place before write operation is complete
Write after read (WAR), or antidependency
  An instruction reads a register or memory location
  Succeeding instruction writes to the location
  Hazard occurs if the write operation completes before the read operation takes place
Write after write (WAW), or output dependency
  Two instructions both write to the same location
  Hazard occurs if the write operations take place in the reverse order of the intended sequence
Notes: There are three types of data hazards;
• Read after write (RAW), or true dependency: An instruction modifies a register or memory location and a succeeding instruction reads the data in that memory or register location. A hazard occurs if the read takes place before the write operation is complete.
• Write after read (WAR), or antidependency: An instruction reads a register or memory location and a succeeding instruction writes to the location. A hazard occurs if the write operation completes before the read operation takes place.
• Write after write (WAW), or output dependency: Two instructions both write to the same location. A hazard occurs if the write operations take place in the reverse order of the intended sequence.
The example of Figure 14.16 is a RAW hazard. The other two hazards are best discussed in the context of superscalar organization, discussed in Chapter 16.

## Slide 31: Control Hazard
Also known as a branch hazard
Occurs when the pipeline makes the wrong decision on a branch prediction
Brings instructions into the pipeline that must subsequently be discarded
Dealing with Branches:
  Multiple streams
  Prefetch branch target
  Loop buffer
  Branch prediction
  Delayed branch
Notes: A control hazard, also known as a branch hazard, occurs when the pipeline makes the wrong decision on a branch prediction and therefore brings instructions into the pipeline that must subsequently be discarded. We discuss approaches to dealing with control hazards next.
One of the major problems in designing an instruction pipeline is assuring a steady flow of instructions to the initial stages of the pipeline. The primary impediment, as we have seen, is the conditional branch instruction. Until the instruction is actually executed, it is impossible to determine whether the branch will be taken or not.
A variety of approaches have been taken for dealing with conditional branches:
Multiple streams
Prefetch branch target
Loop buffer
Branch prediction
Delayed branch

## Slide 32: Multiple Streams
A simple pipeline suffers a penalty for a branch instruction because it must choose one of two instructions to fetch next and may make the wrong choice
A brute-force approach is to replicate the initial portions of the pipeline and allow the pipeline to fetch both instructions, making use of two streams
Drawbacks:
With multiple pipelines there are contention delays for access to the registers and to memory
Additional branch instructions may enter the pipeline before the original branch decision is resolved
Notes: 42
A simple pipeline suffers a penalty for a branch instruction because it must choose one of two instructions to fetch next and may make the wrong choice. A brute-force approach is to replicate the initial portions of the pipeline and allow the pipeline to fetch both instructions, making use of two streams. There are two problems with this approach:
  With multiple pipelines there are contention delays for access to the registers and to memory.
  Additional branch instructions may enter the pipeline (either stream) before the original branch decision is resolved. Each such instruction needs an additional stream.
  Despite these drawbacks, this strategy can improve performance. Examples of machines with two or more pipeline streams are the IBM 370/168 and the IBM 3033.

## Slide 33: Prefetch Branch Target
When a conditional branch is recognized, the target of the branch is prefetched, in addition to the instruction following the branch
Target is then saved until the branch instruction is executed
If the branch is taken, the target has already been prefetched
IBM 360/91 uses this approach
Notes: 43
When a conditional branch is recognized, the target of the branch is prefetched, in addition to the instruction following the branch. This target is then saved until the branch instruction is executed. If the branch is taken, the target has already been prefetched.
The IBM 360/91 uses this approach.

## Slide 34: Loop Buffer
Small, very-high speed memory maintained by the instruction fetch stage of the pipeline and containing the n most recently fetched instructions, in sequence
Benefits:
  Instructions fetched in sequence will be available without the usual memory access time
  If a branch occurs to a target just a few locations ahead of the address of the branch instruction, the target will already be in the buffer
  This strategy is particularly well suited to dealing with loops
  Similar in principle to a cache dedicated to instructions
  Differences:
    The loop buffer only retains instructions in sequence
    Is much smaller in size and hence lower in cost
Notes: 44
A loop buffer is a small, very-high-speed memory maintained by the instruction fetch stage of the pipeline and containing the n most recently fetched instructions, in sequence. If a branch is to be taken, the hardware first checks whether the branch target is within the buffer. If so, the next instruction is fetched from the buffer. The loop buffer has three benefits:
1. With the use of prefetching, the loop buffer will contain some instruction sequentially ahead of the current instruction fetch address. Thus, instructions fetched in sequence will be available without the usual memory access time.
2. If a branch occurs to a target just a few locations ahead of the address of the branch instruction, the target will already be in the buffer. This is useful for the rather common occurrence of IF–THEN and IF–THEN–ELSE sequences.
3. This strategy is particularly well suited to dealing with loops, or iterations; hence the name loop buffer. If the loop buffer is large enough to contain all the instructions in a loop, then those instructions need to be fetched from memory only once, for the first iteration. For subsequent iterations, all the needed instructions are already in the buffer.
The loop buffer is similar in principle to a cache dedicated to instructions. The differences are that the loop buffer only retains instructions in sequence and is much smaller in size and hence lower in cost.

## Slide 35: Branch Prediction
Various techniques can be used to predict whether a branch will be taken:
  Predict never taken
  Predict always taken
  Predict by opcode
  Taken/not taken switch
  Branch history table
  These approaches are static
  They do not depend on the execution history up to the time of the conditional branch instruction
  These approaches are dynamic
  They depend on the execution history
Notes: 45
Various techniques can be used to predict whether a branch will be taken. Among the more common are the following:
• • • • •
Predict never taken
Predict always taken
Predict by opcode
Taken/not taken switch
Branch history table
The first three approaches are static: they do not depend on the execution history up to the time of the conditional branch instruction. The latter two approaches are dynamic: They depend on the execution history.
The first two approaches are the simplest. These either always assume that the branch will not be taken and continue to fetch instructions in sequence, or they always assume that the branch will be taken and always fetch from the branch tar- get. The predict-never-taken approach is the most popular of all the branch prediction methods.
Studies analyzing program behavior have shown that conditional branches are taken more than 50% of the time [LILJ88], and so if the cost of prefetching from either path is the same, then always prefetching from the branch target address should give better performance than always prefetching from the sequential path. However, in a paged machine, prefetching the branch target is more likely to cause a page fault than prefetching the next instruction in sequence, and so this performance penalty should be taken into account. An avoidance mechanism may be employed to reduce this penalty.
The final static approach makes the decision based on the opcode of the branch instruction. The processor assumes that the branch will be taken for certain branch opcodes and not for others. [LILJ88] reports success rates of greater than 75% with this strategy.
Dynamic branch strategies attempt to improve the accuracy of prediction by recording the history of conditional branch instructions in a program. For example, one or more bits can be associated with each conditional branch instruction that reflect the recent history of the instruction. These bits are referred to as a taken/ not taken switch that directs the processor to make a particular decision the next time the instruction is encountered. Typically, these history bits are not associated with the instruction in main memory. Rather, they are kept in temporary high- speed storage. One possibility is to associate these bits with any conditional branch instruction that is in a cache. When the instruction is replaced in the cache, its history is lost. Another possibility is to maintain a small table for recently executed branch instructions with one or more history bits in each entry. The processor could access the table associatively, like a cache, or by using the low-order bits of the branch instruction’s address.

## Slide 36: Intel 80486 Pipelining
Fetch
Objective is to fill the prefetch buffers with new data as soon as the old data have been consumed by the instruction decoder
Operates independently of the other stages to keep the prefetch buffers full
Decode stage 1
All opcode and addressing-mode information is decoded in the D1 stage
3 bytes of instruction are passed to the D1 stage from the prefetch buffers
D1 decoder can then direct the D2 stage to capture the rest of the instruction
Decode stage 2
Expands each opcode into control signals for the ALU
Also controls the computation of the more complex addressing modes
Execute
Stage includes ALU operations, cache access, and register update
Write back
Updates registers and status flags modified during the preceding execute stage
Notes: An instructive example of an instruction pipeline is that of the Intel 80486. The 80486 implements a five-stage pipeline:
Fetch: Instructions are fetched from the cache or from external memory and placed into one of the two 16-byte prefetch buffers. The objective of the fetch stage is to fill the prefetch buffers with new data as soon as the old data have been consumed by the instruction decoder. Because instructions are of variable length (from 1 to 11 bytes not counting prefixes), the status of the prefetcher relative to the other pipeline stages varies from instruction to instruction. On average, about five instructions are fetched with each 16-byte load [CRAW90]. The fetch stage operates independently of the other stages to keep the prefetch buffers full.
Decode stage 1: All opcode and addressing-mode information is decoded in the D1 stage. The required information, as well as instruction-length information, is included in at most the first 3 bytes of the instruction. Hence, 3 bytes are passed to the D1 stage from the prefetch buffers. The D1 decoder can then direct the D2 stage to capture the rest of the instruction (displacement and immediate data), which is not involved in the D1 decoding.
Decode stage 2: The D2 stage expands each opcode into control signals for the ALU. It also controls the computation of the more complex addressing modes.
Execute: This stage includes ALU operations, cache access, and register update.
Write back: This stage, if needed, updates registers and status flags modified during the preceding execute stage. If the current instruction updates memory, the computed value is sent to the cache and to the bus-interface write buffers at the same time.
With the use of two decode stages, the pipeline can sustain a throughput of close to one instruction per clock cycle. Complex instructions and conditional branches can slow down this rate.

## Slide 37
Notes: The register organization includes the following types of registers (Table 14.2):
• General: There are eight 32-bit general-purpose registers (see Figure 14.3c). These may be used for all types of x86 instructions; they can also hold operands for address calculations. In addition, some of these registers also serve special purposes. For example, string instructions use the contents of the ECX, ESI, and EDI registers as operands without having to reference these registers explicitly in the instruction. As a result, a number of instructions can be encoded more compactly. In 64-bit mode, there are 16 64-bit general-purpose registers.
• Segment: The six 16-bit segment registers contain segment selectors, which index into segment tables, as discussed in Chapter 8. The code segment (CS) register references the segment containing the instruction being executed. The stack segment (SS) register references the segment containing a user-visible stack. The remaining segment registers (DS, ES, FS, GS) enable the user to reference up to four separate data segments at a time.
• Flags: The 32-bit EFLAGS register contains condition codes and various mode bits. In 64-bit mode, this register is extended to 64 bits and referred
to as RFLAGS. In the current architecture definition, the upper 32 bits of RFLAGS are unused.
Instruction pointer: Contains the address of the current instruction.
There are also registers specifically devoted to the floating-point unit:
Numeric: Each register holds an extended-precision 80-bit floating-point number. There are eight registers that function as a stack, with push and pop operations available in the instruction set.
Control: The 16-bit control register contains bits that control the operation of the floating-point unit, including the type of rounding control; single, double, or extended precision; and bits to enable or disable various exception conditions.
Status: The 16-bit status register contains bits that reflect the current state of the floating-point unit, including a 3-bit pointer to the top of the stack; condition codes reporting the outcome of the last operation; and exception flags.
Tagword: This 16-bit register contains a 2-bit tag for each floating-point numeric register, which indicates the nature of the contents of the corresponding register.
The four possible values are valid, zero, special (NaN, infinity, denormalized), and empty. These tags enable programs to check the contents of a numeric register without performing complex decoding of the actual data in the register. For example, when a context switch is made, the processor need not save any floating-point registers that are empty.
The use of most of the aforementioned registers is easily understood. Let us elaborate briefly on several of the registers.

## Slide 38: Summary
Processor organization
Register organization
  User-visible registers
  Control and status registers
Instruction cycle
  The indirect cycle
  Data flow
The x86 processor family
  Register organization
  Interrupt processing
Instruction pipelining
  Pipelining strategy
  Pipeline performance
  Pipeline hazards
  Dealing with branches
  Intel 80486 pipelining
Chapter 14
Processor Structure and Function
Notes: Chapter 14 summary.