## Slide 1: Computer Architecture and Logic Design (CALD) Lecture 03
Engr.Ramsha Mashood
Senior Lecturer
Department of Software Engineering
Bahria University Karachi Campus
Email: sorathhansrajani.bukc@bahria.edu.pk

## Slide 2: Moore’s Law
Increased density of components on chip
Gordon Moore – co-founder of Intel
Number of transistors on a chip will double every year
Since 1970’s development has slowed a little
  Number of transistors doubles every 18 months
Cost of a chip has remained almost unchanged
Higher packing density means shorter electrical paths, giving higher performance
Smaller size gives increased flexibility
Reduced power and cooling requirements
Fewer interconnections increases reliability

## Slide 3: Growth in CPU Transistor Count

## Slide 4: Microprocessor Speed
Pipelining:
  Multiple stages of operation including fetching the instruction, decoding the opcode, fetching operands, performing a calculation, and so on..
  Pipelining enables a processor to work simultaneously on multiple instructions.
  For example: while one instruction is being executed, the computer is decoding the next instruction.
Branch prediction:
  The processor looks ahead in the instruction code fetched from memory and predicts which branches or group of instructions, are likely to be processed next.
  Prefetches the correct instructions and buffer them so that the processor is kept busy.
Superscalar execution:
  Ability to issue more than one instruction in every processor clock cycle.
  Multiple parallel pipelines are used.

## Slide 5: Microprocessor Speed
Data flow analysis:
  The processor analyses which instructions are dependent on each other's results, or data, to create an optimized schedule of instructions.
  Prevents unnecessary delay.
Speculative execution:
  Using branch prediction and data flow analysis, some processors speculatively executes instructions ahead of their actual appearance in the program execution, holding the results in temporary locations.
  Enabling processors to keep their execution engines as busy as possible by executing instructions that are likely to be needed.

## Slide 6: Performance Balance
While processor speed has grown rapidly, the speed with which data can be transferred between main memory and the processor has lagged badly.
The interface between processor and main memory is the most crucial pathway in the entire computer because it is responsible for carrying a constant flow of program instructions and data between memory chips and the processor.
If memory or the pathway fails to keep pace with the processor’s insistent demands, the processor stalls in a wait state, and valuable processing time is lost

## Slide 7: Some Solution
■ Increase the number of bits that are retrieved at one time by making DRAMs “wider” rather than “deeper” and by using wide bus data paths.
■ Change the DRAM interface to make it more efficient by including a cache1 or other buffering scheme on the DRAM chip.
■ Reduce the frequency of memory access by incorporating increasingly complex and efficient cache structures between the processor and main memory. This includes the incorporation of one or more caches on the processor chip as well as on an off-chip cache close to the processor chip.

## Slide 8: Continue..
Increase the interconnect bandwidth between processors and memory by using higher-speed buses and a hierarchy of buses to buffer and structure data flow.
Another area of design focus is the handling of I/O devices.

## Slide 9
Another area of design focus is the handling of I/O devices.

## Slide 10: Improvements in Chip Organization and Architecture
Increase hardware speed of processor
  Fundamentally due to shrinking logic gate size
    More gates, packed more tightly, increasing clock rate
    Propagation time for signals reduced
Increase size and speed of caches
  Dedicating part of processor chip
    Cache access times drop significantly
Change processor organization and architecture
  Increase effective speed of execution
  Parallelism

## Slide 11: Amdahl’s Law
Amdahl’s law was first proposed by Gene Amdahl in 1967
deals with the potential speedup of a program using multiple processors

## Slide 12
This equation is illustrated in Figures 2.3 and 2.4. Two important conclusions can be drawn:
1. When f is small, the use of parallel processors has little effect.
2. As N approaches infinity, speedup is bound by 1/(1 - f), so that there are diminishing returns for using more processors

## Slide 13
Amdahl’s law can be generalized to evaluate any design or technical improvement in a computer system. Consider any enhancement to a feature of a system that results in a speedup. The speedup can be expressed as

## Slide 14
Suppose that a feature of the system is used during execution a fraction of the time f, before enhancement, and that the speedup of that feature after enhancement is SUf. Then the overall speedup of the system is

## Slide 15: Example 1

## Slide 16: Diminishing Returns
Internal organization of processors complex
  Can get a great deal of parallelism
  Further significant increases likely to be relatively modest
Benefits from cache are reaching limit
Increasing clock rate runs into power dissipation problem
  Some fundamental physical limits are being reached

## Slide 17: System Clock
Performance is one of the key parameters to consider, along with cost, size, security, reliability, and power consumption (in some cases).
Operations performed by a processor (fetching, decoding, execution), are governed by a system clock.
All operations begin with the pulse of the clock.

## Slide 18: Computer Performance Measures – Clock Speed
The execution of an instruction involves a number of discrete steps, such as
Fetching the instruction from memory
Decoding the various portions of the instruction
Loading and storing data
Performing arithmetic and logical operations.

## Slide 19: Computer Performance Measures – Clock Speed
Clock rate or clock speed:
  Pulse frequency or the rate of pulses produced by the clock.
  Measured in number of cycles per second or Hertz (Hz).
Clock cycle or clock tick:
  One increment, or pulse of the clock.
Cycle time:
  The time between pulses (t = 1/f).

## Slide 20: Problems with Clock Speed and Login Density
Power
  Power density increases with density of logic and clock speed
  Dissipating heat
RC delay
  Speed at which electrons flow limited by resistance and capacitance of metal wires connecting them
  Delay increases as RC product increases
  Wire interconnects thinner, increasing resistance
  Wires closer together, increasing capacitance
Memory latency
  Memory speeds lag processor speeds
Solution:
  More emphasis on organizational and architectural approaches

## Slide 21: Computer Performance Measures – Instruction Execution Rate
CPI:
  Average number of cycles per instruction.
MIPS:
  Millions of Instructions per second.
FLOPS or MFLOPS:
  Floating point operations per second or
  Millions of floating-point operations per second.

## Slide 22: Instruction Execution Rate
Let CPIi be the number of cycles required for instruction type i, and Ii be the number of executed instructions of type i for a given program. Then we can calculate an overall CPI as follows

## Slide 23: Instruction Execution Rate
p is the number of processor cycles needed to decode and execute the instruction
m is the number of memory references needed
k is the ratio between memory cycle time and processor cycle time.
The five performance factors in the preceding equation (Ic, p, m, k, t) are influenced by four system attributes: the design of the instruction set (known as instruction set architecture

## Slide 24: MIPS RATE
A common measure of performance for a processor is the rate at which instructions are executed, expressed as millions of instructions per second (MIPS), referred to as the MIPS rate. We can express the MIPS rate in terms of the clock rate and CPI as follows